## Slide 1: CPU Architecture SW-HW
Amichai Ben-David

## Slide 2: Program to Machine Code
C/assembly
Compile
Linker
Assembler
Machine code
System Verilog
Notes: SDK – Software development Kit של RISCV מפותח ופשוט לשימוש. בשלב הראשון - צריך לכתוב קוד בC.

## Slide 3: Program to Machine Code
C/assembly
Compile
Linker
Assembler
Machine code
System Verilog
Notes: אותו האסמבלי צריך להתמע בתוך מערכת גדולה יותר – מעטפת של מערכת הפעלה או קרנל kernal.

## Slide 4: Program to Machine Code
C/assembly
Compile
Linker
Assembler
Machine code
System Verilog
Notes: אותה חבילת SDK של GCC ניתן גם להמיר את הELF לפורמט Systemverilog לטעינת ROM או TAP וכו.

## Slide 5: Program to Machine Code
C/assembly
Compile
Linker
Assembler
Machine code
System Verilog
Notes: אציין שניתן למסך את כל התהליך הזה באמצעות לקיחת סיפריות linker קיימות ללא צורך בעריכה וירידה לרמה כזו של Toolchain – אבל כאשר רוצים לפתח מעבד לבד זה דיי הכרחי.

## Slide 6: SS_RVC ISA – Instruction Set Architecture
In the “Subset RISCV Core“ we will support 3 instruction formats:
R-Type: Register<->Register operations (add,xor,or,and…) Example: add x3, x2, x1
I-Type: Register<->immediate operations(addi,xori,ori,andi…) Example: addi x3, x2, 1234
S-Type: Store Words to Memory Example: sw x3, 8(x2)

## Slide 7: SS_RVC ISA – Instruction Set Architecture
The Subset RISCV ISA – Design Camp
S-Type
I-Type
R-Type

## Slide 8: SS_RVC Hardware
Load Instruction memory before program starts the execution.

## Slide 9: SS_RVC Hardware
PC
Instruction Fetch
  Program counter fitch.
  Get the 32 bit instruction

## Slide 10: SS_RVC Hardware
Instruction Fetch
  Program counter fitch.
  Get the 32 bit instruction

## Slide 11: SS_RVC Hardware
Rs1 Rs2
Instruction Fetch
  Program counter fitch.
  Get the 32 bit instruction
Instruction Decode
  Read Register file
  Detects Opcode and Set Ctrl Bits

## Slide 12: SS_RVC Hardware
Data1 Data2
Instruction Fetch
  Program counter fitch.
  Get the 32 bit instruction
Instruction Decode
  Read Register file
  Detects Opcode and Set Ctrl Bits
Execute
  Logic / Arithmetic operation on the data

## Slide 13: SS_RVC Hardware
Write Back
Instruction Fetch
  Program counter fitch.
  Get the 32 bit instruction
Instruction Decode
  Read Register file
  Detects Opcode and Set Ctrl Bits
Execute
  Logic / Arithmetic operation on the data
Write Back
  Data write to the “Destination Register”

## Slide 14: 4 Stage Pipe-Line
ADD x1, x2, x3
ADDI x4, x5, 300
XOR x5, x7, x8
SW x9, 8(x0)
0x0
0x0
0x4
0x8
0xC

## Slide 15: 4 Stage Pipe-Line
ADD x1, x2, x3
ADDI x4, x5, 300
XOR x5, x7, x8
SW x9, 8(x0)
0x4
0x0
0x0
0x4
0x8
0xC

## Slide 16: 4 Stage Pipe-Line
ADD x1, x2, x3
ADDI x4, x5, 300
XOR x5, x7, x8
SW x9, 8(x0)
0x8
0x4
0x0
0x4
0x8
0xC

## Slide 17: 4 Stage Pipe-Line
ADD x1, x2, x3
ADDI x4, x5, 300
XOR x5, x7, x8
SW x9, 8(x0)
0xC
0x8
0x0
0x4
0x8
0xC

## Slide 18: 4 Stage Pipe-Line
ADD x1, x2, x3
ADDI x4, x5, 300
XOR x5, x7, x8
SW x9, 8(x0)
0x10
0xC
0x0
0x4
0x8
0xC

## Slide 19: Data Hazards
The HW Should Support “Data Hazard”. A Hazard occurs when first instruction will update a register value, but the next instruction is already reading the “old” data.
xor x2, x1, x3 //x2 = x1 ^ x3
addi x3, x2, 15 //x3 = x2 + 15
Or x1, x3, x1 //x1 = x3 | x2
Solving the Hazards can be done using a “forwarding Unit”.

## Slide 20: Data Hazards
xor x2,x1,x3
addi x3,x2,15
or x1,x3,x1
xor x2, x1, x3
addi x3, x2, 15
Or x1, x3, x1

## Slide 21: Modern CPU Architecture
Youtube - Modern CPU Architecture Part 2
Youtube - Modern CPU Architecture Part 1

## Slide 22: Getting Started with MAS
Describe in a diagram the Data path
  I-Type Data path
  R-Type Data path
  S-Type Data path
Understand where are the control bits needed
  Selector on Muxes
  Flip Flop Enables
Design the “Decode Table”
  Input : Instruction (opcodes & Funct3/7)
  Output : Control bits
Solve Data Hazards in HW.