## Slide 1: Cache Concepts
Amichai Ben-David

## Slide 2: Cache Concepts – we want to discuss
Cache Associativity:
Direct Mapping
Fully associative
16/8/4-way associative
Physical Memory address – DDR RAM
TAG, SET, Offset, Way, CL
MESI
Snoops – Example: SnpInv, SnpRd, SnpData,
Partial Write
Fill
Prefetch
Silent Evict , Clean Evict ,Dirty Evict
Write Back
Clean Data forwarding
Cache 2 Cache forwarding

## Slide 3: But first:

## Slide 4: Cache structure example
Core: Request Cache lookup: - LOAD (Read)
- STORE (Write)

## Slide 5: Cache structure example
Far Memory: From cache point of view - The “full” data structure. - higher level of cache
DDR (DRAM)
May be distributed memory.

## Slide 6: Cache structure example
Transaction Queue (TQ)
Follows the “life cycle” of transactions. Classic implementation is FSM per entry.

## Slide 7: Cache structure example
Tag Array
Maps the full Physical memory to the cache structure.

## Slide 8: Cache structure example
Data Cache Array

## Slide 9: Cache structure example
Cache Pipe

## Slide 10: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 11: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 12: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 13: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 14: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 15: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 16: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 17: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 18: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 19: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 20: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 21: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 22: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 23: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 24: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 25: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 26: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 27: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 28: Cache
Memory - 4GB
Cache Size - 256KB
Set[9:0] - 1024 rows
Tag[15:0] - 16’b Tag
Way[1:0] - 4 ways in Set
Cache-Line (CL) - 64B
Tag Array Size:
(#Set)x(#Way)x(#TAG)
1024x4x16 = 65536 bit =
8192 Byte = 2^13 = 8KB
Data Array Size:
(#Set)x(#Way)x(#CL)
1024x4x512 = 2097152 bit =
262144 Byte = 2^18 = 256KB
[31:16] [15:6] [5:0]
Address[31:0]
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 29: Cache - Example
Read Look-up Example: Address[31:0] = {16’d5 , 10’d3 , 6’d0} -> Tag=5 , Set=3 , Offset=0
Read Set from Table
Check If a way matches TAG
Concatenate ‘way’ to make Cache Data array Address: DataArrayPtr[17:0] = {2’d1 , 10’d3 , 6’d0}
Read the DataArray
[31:16] [15:6] [5:0]
Address[31:0]
5
17
8
13
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 30: Cache - Example
Read Look-up Example: Address[31:0] = {16’d5 , 10’d3 , 6’d0} -> Tag=5 , Set=3 , Offset=0
Read Set from Table
Check If a way matches TAG
Concatenate ‘way’ to make Cache Data array Address: DataArrayPtr[17:0] = {2’d1 , 10’d3 , 6’d0}
Read the DataArray
[31:16] [15:6] [5:0]
Address[31:0]
5
17
8
13
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 31: Cache - Example
Read Look-up Example: Address[31:0] = {16’d5 , 10’d3 , 6’d0} -> Tag=5 , Set=3 , Offset=0
Read Set from Table
Check If a way matches TAG
Concatenate ‘way’ to make Cache Data array Address: DataArrayPtr[17:0] = {2’d1 , 10’d3 , 6’d0}
Read the DataArray
[31:16] [15:6] [5:0]
Address[31:0]
5
17
8
13
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 32: Cache - Example
Read Look-up Example: Address[31:0] = {16’d5 , 10’d3 , 6’d0} -> Tag=5 , Set=3 , Offset=0
Read Set from Table
Check If a way matches TAG
Concatenate ‘way’ to make Cache Data array Address: DataArrayPtr[17:0] = {2’d1 , 10’d3 , 6’d0}
Read the DataArray
[31:16] [15:6] [5:0]
Address[31:0]
5
17
8
13
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 33: Cache - Example
Read Look-up Example: Address[31:0] = {16’d5 , 10’d3 , 6’d0} -> Tag=5 , Set=3 , Offset=0
Read Set from Table
Check If a way matches TAG
Concatenate ‘way’ to make Cache Data array Address: DataArrayPtr[17:0] = {2’d1 , 10’d3 , 6’d0}
Read the DataArray
[31:16] [15:6] [5:0]
Address[31:0]
5
17
8
13
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 34: Cache - Example
Read Look-up Example: Address[31:0] = {16’d5 , 10’d3 , 6’d0} -> Tag=5 , Set=3 , Offset=0
Read Set from Table
Check If a way matches TAG
Concatenate ‘way’ to make Cache Data array Address: DataArrayPtr[17:0] = {2’d1 , 10’d3 , 6’d0}
Read the DataArray
[31:16] [15:6] [5:0]
Address[31:0]
5
17
8
13
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]

## Slide 35: Cache - Example
Read Look-up Example: Address[31:0] = {16’d5 , 10’d3 , 6’d0} -> Tag=5 , Set=3 , Offset=0
Read Set from Table
Check If a way matches TAG
Concatenate ‘way’ to make Cache Data array Address: DataArrayPtr[17:0] = {2’d1 , 10’d3 , 6’d0}
Read the DataArray
[31:16] [15:6] [5:0]
Address[31:0]
5
17
8
13
DataArrayPtr[17:0]
[17:16] [15:6] [5:0]
64 Byte CL

## Slide 36: Block Diagram
The Cache has 4 unites:
  Transaction Queue (TQ)
  Pipe
  Tag Array (Given as HIP)
  Data Cache Array (Given as HIP)

## Slide 37: Block Diagram
The Cache has 4 unites:
  Transaction Queue (TQ)
  Pipe
  Tag Array (Given as HIP)
  Data Cache Array (Given as HIP)

## Slide 38: TQ Entry State Machine:
TQ FSM - Write Hit/Miss Flow:
IDLE
  TQ Entry is a valid candidate for new allocation from Core READ/WRITE requests.
CORE_WR_REQ
  A write request from core will allocate an IDLE entry in the TQ.
  Each entry has a “buffer” with the Write address, Data & ReqID.
  Once Allocated, the TQ entry is a candidate for Pipe lookup
LU_CORE_WR_REQ
  The Pipe arbiter choose this entry for Pipe lookup.
  Waiting for Pipe acknowledge to move back to IDLE
  Pipe may reject and move to back to “CORE_WR_REQ”

## Slide 39: TQ Entry State Machine:
TQ FSM - Read Hit Flow:
IDLE
  TQ Entry is a valid candidate for new allocation from Core READ/WRITE requests.
CORE_RD_REQ
  A read request from core will allocate an IDLE entry in the TQ.
  Each entry has a “buffer” with the Read address, data & ReqID.
  Once Allocated, the TQ entry is a candidate for Pipe lookup
LU_CORE_RD_REQ
  The Pipe arbiter choose this entry for Pipe lookup.
  Waiting for Pipe Read response with data to move to “CORE_RD_RSP”
  Pipe may reject and move back to “CORE_READ_REQ”
CORE_RD_RSP
  TQ Entry is a valid Candidate for Read Response Arbiter towards the Core

## Slide 40: TQ Entry State Machine:
TQ FSM - Read Miss Flow:
IDLE
CORE_RD_REQ
LU_CORE_RD_REQ
FM_RD_REQ
  TQ Entry is a valid Candidate for Read Request Arbiter towards the FM
WAIT_FILL
  Read Request was sent to FM, Waiting for response.
FILL
  Got Read response with data from FM.
  Valid Candidate for pipe lookup. (which will write the Fill data)
LU_FILL
  The Pipe arbiter choose this entry for Pipe lookup.
  Waiting for Pipe acknowledge to move back to IDLE

## Slide 41: Write Cache Hit
Write Request
Write Request
Write Request
Write Request
Write Request
Write Request
Tag Hit
Aloc Entry
De-Aloc Entry
Write Request

## Slide 42: Read Cache Hit
Aloc Entry
De-Aloc Entry
Tag Hit

## Slide 43: Read Cache Miss
Aloc Entry
De-Aloc Entry
Tag Hit

## Slide 44: Pipe Stages & Outcomes
The Pipe has 6 Steps in 2-6 Pipe Stages. (Implementation Specific)
3 Types of Lookup request: (1) Read (2) Write (3) Fill
8 Possible Flows in the Pipe

## Slide 45: Cache Concepts – we want to discuss
Cache Associativity:
Direct Mapping
Fully associative
16/8/4-way associative
Physical Memory address – DDR RAM
TAG, SET, Offset, Way, CL
MESI
Snoops – Example: SnpInv, SnpRd, SnpData,
Partial Write
Fill
Prefetch
Silent Evict , Clean Evict ,Dirty Evict
Write Back
Clean Data forwarding
Cache 2 Cache forwaring